## Slide 1: Microseismic event localization using both wavefields and their spatial gradients
Zhenhua Li* and Mirko van der Baan
University of Alberta

## Slide 2: Microseismic monitoring
1. Human-activity related
(mining, oil/gas production)
2. Very small magnitude
(smaller than 0)
3. Indication of fracture development
(accurate determination of
microseismic event locations)
Color coding: hydraulic fracture stages
Microseismicity :

## Slide 3: Microseismic event localization
Example of surface array microseismic record
Ray-based method :
P- and S-wave first arrival picking
Polarization analysis for all the pickings
(incident direction)
3. Travel time inversion based methods
Advantages:
Fast algorithms
Less computation requirement
Drawbacks:
Picking errors from miss-picking and inaccurate picking
Manual picking can be very time-consuming (especially for surface array)
High frequency approximation is seriously affected by medium velocity errors
P
S

## Slide 4: Microseismic event localization
What will happen if you shout to the wall
Fink, 1999

## Slide 5: Microseismic event localization
Forward
Time-reversal
seismic source
Estimated source
Reverse-time-extrapolation (RTE) based method :
Injecting full 3C elastic recordings into the estimated medium
Focusing criterion (where and when)
Advantages:
No picking needed
Stacking increases image signal-to-noise ratio
Simple algorithm
Limitations:
Relatively accurate velocity
Computationally intensive (Parallel computing)
May introduce artifacts for vertical borehole recordings for traditional RTE based method

## Slide 6
Example - Homogeneous acoustic model with noiseless data
3C receivers
Explosive point source
Ghost focus
We want to
Keep advantages of RET based methods
Remove ghost focus
How?
By combining both wavefields and their spatial gradients

## Slide 7: How?
3-component geophone
hydrophone
Acoustic
3-component geophone
3-component rotational sensor
Elastic
wavefield
Spatial gradient
The acoustic/elastic representation theorem

## Slide 8: The body force equivalence of seismic source
(Aki and Richards, 2002, chapter 3, eq. 3.3)
Wavefield
Spatial gradient of the wavefield

## Slide 9
2D acoustic reverse time extrapolation
3C particle velocity/displacement back-propagation image
Pressure wavefield back-propagation image

## Slide 10
2D acoustic reverse time extrapolation
Back-propagated pressure wavefield
Acoustic Sink
Measured particle displacement/velocity
Measured pressure field

## Slide 11
2D elastic reverse time extrapolation
3C particle velocity/displacement back-propagation image
3C rotational wavefield back-propagation image

## Slide 12
2D elastic reverse time extrapolation
Measured Rotational motion with translational Green’s function
Measured translational motion with rotational Green’s function
Reconstructed backpropagation translational wavefield
Sink
The first time we involve rotational signal in reverse-time extrapolation

## Slide 13
Focusing criterion (2D)
The Hough transform （HT）
Shape detection (Circle)
Value Accumulation
The Hough image
Original image

## Slide 14
Z
X
t
Z
X
t
Z
X
t
Focusing criterion (2D)
Summation image

## Slide 15
Focusing criterion (2D)
Spatial Coordinates (X,Z)
Summation Magnitude
Corresponding Time
Minimum distance to receivers
Maxima on each summation image
Magnitude
Threshold
Estimated microseismic event
Event location
origin Time
Distance
Threshold

## Slide 16: Example - Acoustic
Deviated borehole with an explosive source

## Slide 17: Example - Acoustic
Representation theorem
Tradition

## Slide 18: Example - Elastic
Vertical borehole with a double couple source

## Slide 19: Example - Elastic

## Slide 20
Conclusion
Reverse time extrapolation doesn’t require P- and S- wave first arrival picking
The acoustic focusing criterion can conveniently determine microseismic event location and time
Acoustic case: hydrophone + three-component receivers = > better locations
Elastic case: three-component translational + three
component rotational sensors = > better locations
Flexible combination of wavefields to improve source
image
Surface receivers are more suitable for this method

## Slide 21
We thank the sponsors of the Microseismic Industry Consortium for financial support.
Acknowledgements
Thank You!