## Slide 1
John R Evans
Geophysicist (seismology and seismometry)
U.S. Geological Survey
Portable sensors for rotational ground motion
All truth passes through three stages. First, it is ridiculed. Second, it is violently opposed. Third, it is accepted as being self-evident. — Arthur Schopenhauer (1788 – 1860)
Brace yourselves, here comes stage two ...

## Slide 2
Good News, Bad News: Finally hitting the big time
“Suddenly” we have a plethora of new instruments
  Either in late-stage development ...
    (maybe available now if you have friends);
  In the “production prototype” stage (ditto); or
  Fully available within months
You will hear talks about these and others:
  Kozák and Jedlička have a clear path to a production prototype
  Brokešová and Málek have a production prototype now in use
  Multiple high-precision FOGs available now or soon (iXBlue, Li, ...)
  RLGs coming up fast
  Clever new idea and improvements (Barak, Velikoseltsev, ASL, ...)
Most of today’s talks and some of tomorrow’s are
  about this; examples follow but listen to the talks:

## Slide 3
New iXBlue FOG
BlueSeis-3A manufacturer specifications:
  Interferometric FOG
  Flat from DC to 100 Hz
  Principally broadband weak motion (20 nrad/s/√Hz so
    ~60 nrad/s over 100 s to 10 Hz and ~1 μrad/s from
    10 to 100 Hz)
  Covers much of the strong-motion range too, though
    we know the Earth limit poorly (100 mrad/s clip)
  20 kg; three axes
  IP66 (IP67 ideal, difference is hose versus 1-m immersion)
  miniSEED output via Internet at up to 200 sps
  However, 20 W at 24 V and fairly costly (but not too bad
    for broadband; cf., G-ring)

## Slide 4
Rotaphone: Ready to go
Three “Model D” now vaulted in Long Valley
  Data from The Geysers in a later talk
  Looking at source effects, site nonlinearity, site
    characterization, etc.
  Based on 4.5-Hz geophones (Netherlands); lower
    useful corner ~2 Hz
  Power (mainly the Linux box portion) is to be lowered soon
    for reduced heat and easier deployment (i.e., batteries)
  Parts cost about 8000 USD
  Talk and poster coming

## Slide 5
Fluid Torus of Kozák and Jedlička (and Evans):
Almost ready
Paper is back to BSSA one week ago
  Describes results for existing prototypes
Production-prototype design identified
  Within a year will construct in Prague and fully test
    at ASL against both rotation and translation
Unfortunately Jan and Petr cannot be here
  so I will give their talk

## Slide 6
FOGs have hit the big time
RLGs are making progress
Magnetometers?
Far better MEMS in sight
ATA high-frequency sensor (no Hg)
Translational-sensor arrays are perfecting
Better testing facilities in several places
So now it is time for lots of applications ...
  and for naysayers to get aboard

## Slide 7
... so let the good times roll !
Wider availability of instruments
More opportunities to deploy
More opportunities to demonstrate efficacy
More chances to develop and prove applications
Better test facilities
More fun ...